## Slide 1
FM Generator
Using ICL 8038
Communication Engineering Course Project
SY ET-A Batch B2
Group 3
Name of Students:
Shreyash Bhatkar - 41
Nishit Chaudhari - 55
Ruturaj Desai - 61

## Slide 2
Objectives and Aim
Part 01
Functions of ICL 8038
Part 02
PIN Diagram and Data Sheet
Part 03
Frequency Modulation
Part 04
Simulated Results
Part 05
Individual Efforts and Timeline
Part 06
Conclusion and References
Part 07

## Slide 3
OBJECTIVES
- To do a detailed study of ICL 8038, it’s pin diagram, datasheets and all the functions.
- To generate a vast structures of waveforms, which IC 8038 can generate.
- Produce high accuracy sine, square, triangular, saw tooth and pulse waveforms with a
minimum of external components.
- Then do the frequency modulation of the generated forms of waves using the designed
circuit.
- Function generators are used in the development, test and repair of electronic equipment.
For example, they may be used as a signal source to test amplifiers or to introduce an
error signal into a control loop.

## Slide 4
About ICL 8038
The ICL8038 waveform generator is a monolithic integrated circuit capable of producing high accuracy
sine, square, triangular, sawtooth and pulse waveforms with a minimum of
external components.
The frequency (or repetition rate) can be selected externally from 0.001Hz to more than 300kHz
using either resistors or capacitors, and frequency modulation and sweeping can be accomplished with
an external voltage.
The ICL8038 is fabricated with advanced monolithic technology, using Schottky barrier diodes and thin
film resistors, and the output is stable over a wide range of temperature and supply variations.
These devices may be interfaced with phase locked loop circuitry to reduce
temperature drift to less than 250ppm/oC

## Slide 6
WORKING
- The circuit needs a dual power supply. A +15 -15 power supply as shown in the circuit is enough for the
purpose.
- The frequency of the output wave
form can be adjusted using R7.It must be a 100K Log POT.
- The duty cycle can be adjusted
using R3 , a 1K POT.
- The distortion of the wave form can be adjusted using R5 , a 100K POT.
- Square,triangle & sine waveforms can be obtained simultaneously at pins 9,3,2 respectively

## Slide 7
FREQUENCY MODULATION
- Frequency modulation (FM) is the standard technique for high-fidelity communications as is evident in the received signals of the FM band (88-108 MHz) vs.
the AM band (450-1650Hz).
- The main reason for the improved fidelity is that FM detectors, when properly
designed, are not sensitive to random amplitude variations which are
the dominant part of electrical noise (heard as static on the AM radio).
- Frequency modulation is not only used in commercial radio
broadcasts, but also in police and hospital communications, emergency
channels, TV sound,wireless (cellular) telephone systems, and radio
amateur bands above 30 MHz.

## Slide 8
FREQUENCY MODULATION
- In an FM signal, the frequency of the signal is changed by the modulation
(baseband) signal while its amplitude remains the same.
- In an AM signal,
we now know that it is
the amplitude (or the
envelope)
of the signal that is
changed by the
modulation signal.

## Slide 9
APPLICATIONS
- Frequency modulation is widely used for FM radio broadcasting.
- It is also used in telemetry, radar, seismic prospecting, and monitoring newborns
for seizures via EEG, two-way radio systems, sound synthesis, magnetic
tape-recording systems and some video-transmission systems.
-The main advantages of FM over AM are:
*Improved signal to noise ratio (about 25dB) w.r.t. to man made
interference.
*Smaller geographical interference between neighboring stations.
*Less radiated power.
*Well defined service areas for given transmitter power.

## Slide 10
INDIVIDUAL CONTRIBUTION
- Individual Contribution : All contributed equally in the project. We took
5 meets online and designed the circuit on the meet itself, so everyone
has their own circuit.
- Considering the contrary that we particularly distributed the topics initially
within ourselves so initially we were working on the following:
*Simulation of the circuit on particular software. (SARANG BHANAP)
*IC 8038 and it’s properties. (SHREYASH BHATKAR & RUTURAJ DESAI)
*Connections within the circuit and finding suitable
components.(NISHIT CHAUDHARI & KAPIL BHALE )
And at the end we worked on every objective individually which is
mentioned above.

## Slide 11
CONCLUSION
You can build this circuit on universal PCB board on the wiring, and various
components can see carefully.
For the devices has various polarity should be careful in the assembly circuit.
They include the electrolytic capacitors, potentiometer, resistors and
Pin of the IC is not an error.
But if the model is developed it may have to invest a lot. Which device
has the additional duty is different.
But the important point is to make circuit more stable and Adjustment
to the desired waveform.

## Slide 13
REFERENCES
http://dev-author.kemin.com/ic8083.pdf
http://www.ecs.umass.edu/ece212/ECE212_lab6.pdf(to study more about
fm generator)
https://www.mit.edu/~6.331/icl8038data.pdf (DataSheet)
https://en.wikipedia.org/wiki/Function_generator
https://www.eleccircuit.com/mini-function-generator-circuit-using-icl8038
/#Basic_circuit
https://wwwusers.ts.infn.it/~milotti/Didattica/Segnali/Exp93f.pdf
https://www.mit.edu/~6.331/icl8038data.pdf

## Slide 14
THANK YOU!